## Slide 1: NSRS Modernization Preparing for New Datums
PSLS Annual Conference
January 2024
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486

## Slide 2
Any references to any commercially available hardware or software do not constitute an endorsement or a disapproval of any manufacturers, developers, dealers, or suppliers.
Thanks.

## Slide 3: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)
Notes: -We are the Federal Government’s oldest scientific agency.
-part of the Executive Branch
-I know it can seem kind of strange that NGS is part of the NOS, but the origins of NGS lie with the C&GS.
-we are a “Program Office” of the NOS
Survey of the Coast – 1807
Coast Survey – 1836  in 1871 the agency was tasked by Congress with responsibility to carry geodetic control inland (>150 years)
Coast and Geodetic Survey – 1878
NGS since 1970

## Slide 4: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)
≠
We’re not USGS, we’re NGS
Notes: -as you can read my slide, I like to point that out because over my years at NGS I’ve seen and heard this misunderstanding quite a bit
-don’t worry! it doesn’t offend us! and we do work closely with USGS, but we are separate agencies within totally different departments of the federal government

## Slide 5: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
NSRS
Notes: NGS develops and maintains the National Spatial Reference System, a national coordinate system that provides the foundation for transportation, navigation, land record systems, mapping and charting efforts, and a multitude of scientific and engineering applications
CLICK
You’ve all seen this or some similar graphic I’m sure. That bottom layer… that’s our baby, the NSRS.

## Slide 6: NGS Mission
access… ? = traditionally  marks/disks/objects
= modern and future  NOAA CORS Network (NCN)
via OPUS
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
Notes: Follow up thought
-like it or not, we know that the vast majority of our users are obtaining NSRS coordinates via OPUS
-while that is our plan for the future of primary access, modernized NSRS, as of now the official form of access (specifically to NAVD88) truly is to “touch brass” as they say  meaning occupy a benchmark

## Slide 7
NCN - NOAA CORS Network
1695 sites
241 organizations
Notes: What does that mean?
Please don’t think of this as us here at NGS being some pointy-haired semantics. We need to make distinctions about CORS when talking about all this. If you haven’t already realized this, you’ll start to catch on today.

## Slide 8: CORS Networks
Global: International GNSS Service (IGS) Network
NSRS: NOAA CORS Network (NCN)
Regional: State/Municipal or Private CORS Networks
They’re all semi-coupled, not 100% overlap.
Notes: Global: International GNSS Service (IGS) Network
  The international standard since mid-1990s
  Supported by IGS Analysis Centers (ACs)  NGS is one AC of seven total
  Overall system sponsored by NASA
NSRS: NOAA CORS Network (NCN)
  NGS processes/distributes data, but few are NGS-operated
  Subset of NGS-operated CORS comprise the under construction NOAA Foundation CORS Network (NFCN)
Regional/State/Commonwealth/Local Networks
  Real-Time Networks (RTN… aka “VRS”)
  Currently semi-coupled to the NCN
    NGS sees the future as a close coupling of other networks with the NCN so users can seamlessly and confidently work in the NSRS using their favorite regional/local CORS network

## Slide 9: IGS CORS Network
Source: https://www.igs.org/maps/#station-map
Notes: There are several CORS Networks.
The Global Standard is the IGS Network
  IGS = International GNSS Service
The NOAA CORS Network (NCN) which consists of:
  The NOAA Foundation CORS Network (NFCN), a sub-network being installed, owned, and operated by NGS
  and 2,000+ stations managed, but rarely owned by NGS
Other Regional/Local Networks (RTNs, etc.)
  Currently semi-coupled to the NCN
    NGS sees the future as a close coupling of these other networks with the NCN so users can seamlessly and confidently work in the NSRS using their favorite regional/local CORS network.

## Slide 10: NOAA CORS Network (NCN)
Notes: -I would like to point out we have a new, official name for the network you see represented on this map,
-The NOAA CORS Network, or NCN
CLICK
-this is neat little graphic with some stats on teh NCN you can find on our website
-below the gaphic youll find a search bar with more information

## Slide 11: NOAA CORS Network (NCN) in PA
Notes: where else but the federal government are you going to see two acronyms within one acronym?

## Slide 12: KeyNetGPS CORS Network

## Slide 13: NOAA CORS Network (NCN) in PA

## Slide 14: KeyNetGPS CORS Network
non-NCN CORS

## Slide 15: Online Positioning User Service
      dual frequency receiver
      static observations (via RINEX  ABCD123x.24o)
      30 seconds epoch/logging rate aka recording interval
  OPUS Rapid Static (OPUS-RS)
      15 minutes to 2 hours of GPS data
  OPUS Static (OPUS-S)  also Beta OPUS!
      same requirements as above
      2 to 48 hours of GPS data
  OPUS Projects (OP)
      adds session processing and network adjustment
      training by NGS currently required (~12 hours)
Notes: Currently 4 types of OPUS.
*OPUS only supports GPS constellation data, last I talked to the OPUS developer the plan for incorporation of other constellations is Jan 2021.
Rapid Static – files uploaded that are 15 minutes to 2 hours in duration are processed using an NGS software called “RSGPS”
Static - files that are 2 to 48 hours in duration are processed using an NGS software called PAGES Your coordinates are the average of three independent, single-baseline solutions,
OP and Beta OP - these are not a different processing software, just a way to tie multiple OPUS-Static solutions together and use least squares methods to adjust them all as a coherent network
**the Beta serves as a testing bed for the developers to roll out new features or improvements and get feedback from users

## Slide 16: NGS Products and Services
Not just OPUS
All exist in three environments:
  Development (DEV) - internal testing and development
    same as when you hear a company talk about an “Alpha” product
  Beta - continued internal testing, open for public testing
    key features have already been vetted/tested
  Production - final product, open to public use
    this is what you see first when navigating our website
Notes: I’ll be talking about OPUS today, but I need to clarify one of our processes for this to all be clear. I will also mention that this is a new-ish workflow for NGS, began in the past 8 or so years.
So all NGS Products & Services go thru this process as they are created, tested internally, open for testing by you our constituents, and then rolled out as final products.
CLICK
There’s three environments that products will exist in, listed here in the order they occur
First, a tool will be created on the “DEV” servers for internal NGS-only development, testing, and otherwise “working the bugs out”
this is the same phase as when you hear a software company or video game maker talk about their alpha products
CLICK
Next, after some level of confidence in the product is gained, it will be migrated to the Beta servers, thereby open to the public for their own testing
it’s important to note that when a product is available via our Beta page, when you use it you are indeed now a “beta tester”
key features will have already been tested in the Development environment, but it is still a beta, so as a beta tester please let us know if you have issues/complications/struggles or the like
CLICK
At some point, when all I’s are dotted and T’s crossed, the thing will be moved to the Production environment.
 by then, the tool is integrated into others, has been vetted with 2 testing phases and functions as expected, but may still continue to receive version updates by repeating this process

## Slide 17
www.ngs.noaa.gov
beta.ngs.noaa.gov
Remember, you won’t see the DEV environment…
Notes: So here we have 3 screenshots, first here showing the Production OPUS Projects gateway page
CLICK
Second is the Beta page, with the text here showing the URL for our Beta homepage
-How do you find that beta page? substitute “beta” for “www”
-or most tools that have a beta will have a link to that beta platform
CLICK
Last is the Development or DEV example, which again you will not see unless via a demo from NGS personnel

## Slide 18: Wait… how do I get to the NGS Beta site?

## Slide 19
www.ngs.noaa.gov
beta.ngs.noaa.gov

## Slide 20: OPUS only processes every 30s
You can upload 5s interval data
  But OPUS will trim/decimate to 30s interval
  And this may result in delays or error messages
You can even upload 1s interval data
  But only shorter files, or OPUS kicks it back
Even if you’re running RTK…
  You can setup your base to only log @ 30s rate
  Know your equipment
For static, 30s yields good results
  If using your commercial software, 15s can be advantageous

## Slide 21: OPUS processes every 30s
20s decimates to 60s

## Slide 22
OPUS Rapid Static (OPUS-RS)
  15 min to 2 hours
  Computes atmospheric delay at up to 9 NCN CORS within 250km
  Interpolates that delay to your position
  Reports corrected position with standard deviation stats
OPUS Solution
CORS
5001
Notes: -OPUS Static takes the best 3 of 5 baselines, sequentially processed, and provides you their peak-to-peak average
sidenote
  -we delivered over 1.2 million solutions in 2021, compared to in 2011 when we first broke the 200,000 solutions milestone

## Slide 23
OPUS Rapid Static (OPUS-RS)
15 min to 2 hours
1st creates an atmospheric delay model
2nd position calculated via a DGPS static solution
Notes: OPUS-RS or Rapid Static performs two calculations.
1st - creates an atmospheric delay model from surrounding CORS data (white circle)
2nd - Your position is determined via a differential GPS static solution

## Slide 24
OPUS Static (OPUS-S)
  2 to 48 hours
  Best 3 of 5 baselines
  Sequentially processed
  Reports your peak-to-peak (P2P) average position
5001
OPUS Solution
CORS
5002
Notes: -OPUS Static takes the best 3 of 5 baselines, sequentially processed, and provides you their peak-to-peak average
  -we delivered over 1.2 million solutions in 2021, compared to in 2011 when we first broke the 200,000 solutions milestone
  -sidenote that we’ve already broken the 1.5 million mark for 2022

## Slide 25
OPUS Static (OPUS-S)
  No correlation between your observed marks
  Low Relative Accuracy
  Even if … collected simultaneously
  … and submitted to OPUS simultaneously
  OPUS-S = independent solutions
5001
OPUS Solution
CORS
5002

## Slide 26
OPUS Projects (OP)
  Simultaneous processing of your observed marks
  Improved Relative Accuracy
  Requires more field prep and office processing effort
  OP = true network solutions
  And of course, least squares adjustment
5001
OPUS Solution
CORS
5002
Distant CORS
~400-800 km
5004
5003

## Slide 27: What’s the deal with GPSonBM?
Deadline = 30 September 2023
OPUS Shared Solutions
  2 OPUS-Static, ≥4 hours each
  2 photos of each setup
  Brief Description w/Ties
Progress Dashboard
Web Map Application
GPS on Bench Marks
The struggle is real.
“too much field time”
“we don’t do static”
“poor site, if only we had multi-GNSS”
Notes: Note here that the Dashboard map is separate from the Web Map Application.
CLICK They are linked, but different tools.
If you got mixed up about this at some point, no worries, you were not the only one.
If we have had this process to submit GPSonBM for years now… why are we now putting out this option for OPUS Projects via GVX?
CLICK

## Slide 29: Passive Control
All marks are passive—they sit there and hold a point
Geodetic Control – Terminology
Notes: All marks are passive!—in that they sit there doing nothing in and of themselves besides holding a point
This includes the fixed antenna mount that is a part of a CORS.
But, some marks have permanently installed equipment that enable nearly continuous observations and these are called “active” stations.

## Slide 30
Passive Control

## Slide 31
Terminology - Passive Control
Notes: LZ0930
Lycoming County  PRR copper plug in bridge abutment
--that’s a photo from PennDOT, not sure what District Lycoming County is

## Slide 32
Terminology - Passive Control
Notes: KW0392 –
https://www.ngs.noaa.gov/cgi-bin/ds_mark.prl?PidBox=KW0392
COLUMBIA COUNTY, PA, NEAR READING COMPANY REAILROAD STATION

## Slide 33
Notes: KR1724 - https://www.ngs.noaa.gov/cgi-bin/ds_mark.prl?PidBox=kr1724
Set 1946  Washoe County, NV, about 4 miles southwest of Reno
Recovery 1958  THE STATION MARK WILL BE PRESERVED BY MR. GARCIA, AND WILL BE IN THE CENTER OF HIS LIVING ROOM. - -> BUILT AS A BROKEN WAGON WHEEL WITH THE TRIANGULATION STATION THE HUB THERE-OF.
A STANDARD DISK STAMPED WHEELER 1946, 1958 IS BEING PROVIDED MR. GARCIA, TO PLACE IN THE FLOOR.

## Slide 34: Active Control
Some marks have permanently installed equipment that enables nearly continuous observations
Geodetic Control – Terminology
(they still sit there and hold a point)
Notes: All marks are passive!—in that they sit there doing nothing in and of themselves besides holding a point
This includes the fixed antenna mount that is a part of a CORS.
But, some marks have permanently installed equipment that enable nearly continuous observations and these are called “active” stations.

## Slide 35
Active Control

## Slide 36
Active Control

## Slide 37
Active Control
Active Control

## Slide 38: Active vs. Passive Control
Passive – setting up your RTK Base on existing geodetic control (e.g. Datasheet) while collecting with RTK Rover
Active – setting up your RTK Base to log data while collecting with RTK Rover then processing Base data via OPUS; or collecting with RTN Rover
Geodetic Control – Terminology
My point: surveying is still surveying
Notes: Often the term active geodetic control has been used to mean some equipment is continuously or at least frequently collecting observations at or near a point
Yet those observations are often used to compute coordinates (often time-dependent) at a point on a mark, which, by its nature is passive

## Slide 39: Why OPUS Projects?
Reference Epoch Coordinates (RECs)
  You’ll get coordinates in NATRF2022 and NAPGD2022 on “day one”
  Only “recent” GPS data in the IDB will get RECs
    Federal Register Notice – July 2020
GPS on Benchmarks (GPSonBM)
  3 occupations @ 5 minutes each vs. 2 occupations @ 4 hours each
  Multi-constellation aka “GNSSonBM”

## Slide 40
 | OPUS Shared | OPUS Projects (RINEX) | OPUS Projects (GVX)
Minimum Occupations | 4 hours At least 1, maybe 2* | 2 hours At least 2 | 5 minutes At least 3
Processing | OPUS-S (sequential) | PAGES (simultaneous) | Real Time (RTN/NRTK)
Adjustment | None | Least Squares Network | Least Squares Network
Metadata | 2 photos Brief Description | 3 photos, WinDesc files, Logs, & Report | 3 photos, WinDesc files, Logs, & Report
*Need 2 or more GPS datasets in our database, existing data holdings count toward that.
OPUS Shared vs. OPUS Projects

## Slide 41
Epoch
eh-puck? ee-pock? … to-may-to, to-mah-to
an instant of time; a moment in time
astronomy & geodesy use a decimal date
  2021.4762 = 23 June 2021 @ 19:16:00
  using epochs is important, not your format
    start preparing to assign epochs to your data
Terminology – Time/4D
Notes: -Where do you see an Epoch right now in NGS data?
CLICK
Datasheets! there you see the epoch of 2010.0
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 42
Notes: -Where do you see an Epoch right now in NGS data?
Datasheets! there you see the epoch of 2010.0
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 43
Reference Epoch
Survey Epoch
Notes: -Where do you see an Epoch right now in NGS data?
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 44: Epochs in Modernized NSRS
Reference Epoch (RE)
Position after propagated back in time from SE to RE
Used in NAD 83
REC = RE Coordinate
Ground movement will be hidden
Survey Epoch (SE)
Position at the moment of survey data collection
Used in ITRF
SEC = SE Coordinate
Ground movement will be illustrated

## Slide 45: Yes, we are delayed.
  NSRS Modernization
Notes: So remember, today’s presentation is not JUST about new datums, it is about modernizing the NSRS as a whole.
You don’t know what the NSRS is? Stay tuned, we’ll get there as we go along.

## Slide 46: Delayed Release of the Modernized NSRS
How long will the delay be?
  Our website or newsletter is best source of projected timeframe, current estimate is middle of 2025.
Will the names stay the same?
  Yes, terms containing “2022” such as “NATRF2022” and “NAPGD2022” will remain the same.
Will all previously proposed products be released along with the new datums?
  No, they will not. Check out our June 2022 webinar.
hyperlink to the Track Our Progress homepage
hyperlink to the full FAQ
June 2022 webinar

## Slide 47: Evolution of the NSRS
NAD27
NAD83 (1986)
NAD83 (2011)
Notes: NAD27
-like the dial of a rotary phone, you were out there spinning a theodolite around, running resections and solar shots to get a position… am I right?
-and you’d get a position, but it might not be that great, and if you set a mark then everybody wanted your data, like sharing the old party lines
NAD83(1986)
-we brought in a more accurate network, it was easier to access
-you were using an early total station and data collector, just like pushing the buttons on a touchtone phone
NAD83(2007/2011)
-the network was maturing with more CORS just like the cell towers
-just as cell phones were becoming ubiquitous, so too was the use of OPUS

## Slide 48: Modernized NSRS is our “smartphone”
You resisted it for a while…
It was a little cumbersome to get used to…
But soon you were hooked!
Notes: -so if you think about the NSRS that way, then NATRF2022 is our smartphone, in more ways than one, right?
-some folks were excited to get a smartphone, but some (show of hands?) were reluctant to embrace the idea… kind of like this whole NSRS Modernization deal huh?
-some of us are excited for this development and some folks, well some are ready to retire as soon as NGS rolls this out, am I right?

## Slide 49: Modernizing the NSRS
Updating all NSRS coordinates
  Replace existing datums with new datums
  Replacing existing SPCS83 with new SPCS2022
  Accounting for coordinates changing with time
Improving NGS products and services
Simplifying customer contributions
Making the NSRS:
  More accurate
  More accessible
  More efficient
Rollout in
2025

## Slide 50
Positional Components of
the NSRS
Geometric
aka “Horizontal”
Latitude, Longitude, Ellipsoid Height
Geopotential
aka Orthometric Height
aka “Elevation”
NAD83
NAVD88
Notes: -geometric component is latitude, longitude, and ellipsoid height
-geopotential component is combined with the geometric components to calculate an ortho height or capital H

## Slide 51
NATRF2022
North American Terrestrial Reference Frame of 2022
will replace
NAD83
North American Datum of 1983
Technically, not just NATRF2022 but also its 3 sister TRFs…

## Slide 53: Four TRFs for Modernized NSRS
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 54
Existing, accepted terminology
  International TRF
  first realization of the ITRF was 1992
  NATRF2022 will be based on ITRF2020
“Horizontal Datum” - misnomer for NAD83
  Really is a Geometric Reference Frame
Terrestrial Reference Frame?

## Slide 55
International Terrestrial Reference Frame
(ITRF)
Is native coordinate system for NCN.
Is what OPUS uses.
Is what most of world uses.
Is what NGA aligns WGS-84 to.
Notes: So what is that acronym, ITRF?
-it is a global reference frame, the most widely adopted one, or the “gold standard” or the “Cadillac” or what-have-you
-ITRF is the internationally recognized standard
-who realizes the ITRF? well, NGS contributes to the realization but
CLICK
-The IERS is in responsible charge of defining, realizing and promoting the ITRF
-and the ITRF was formally adopted by the…yes, more acronyms
CLICK
IUGG some years ago

## Slide 56
Watch the grid!
ITRF concept
Epoch:
Notes: Ok, now ITRF mentioned a couple slides ago.
Most simplistic way to explain ITRF is to watch this animation.
This is a very loose representation/visualization of what the ITRF is, a characterization only.

## Slide 57: Four TRFs for Modernized NSRS
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 58: Plate Rotation visualized
Drift…

## Slide 59: Plate-Fixed NSRS TRFs
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
(relative to ITRF)
NA Plate = constant
(relative to NATRF2022)
Notes: We say “NATRF2022” is “fixed” to the N.A. Plate, making it a “plate fixed” frame
-the frame is constant to itself, but rotating within ITRF, and moving in a different direction than the other 3 frames

## Slide 60
ITRF – constant frame, rotating plate

## Slide 61: Plate-Fixed
NATRF – rotating frame, constant with plate

## Slide 62
ITRF or NATRF – your choice if you know epoch
if you know epoch

## Slide 63: Decades of continuously logged GPS data from the NOAA CORS Network (NCN).
  But how?

## Slide 64
NOAA CORS Network (NCN)

## Slide 65: Plate-Fixed
NATRF – rotating frame, constant with plate
= CORS

## Slide 66: Plate-Fixed
ITRF or NATRF
= CORS
Notes: ITRF is independent of any plates, tied to the layer below,
-”plate-agnostic” if we want to sound all silicon valley ish
-the plates go down about 200 km (125 mi) deep below our feet right now, as we’re on a continental plate
--(oceanic plates are roughly half the thickness, like 100 km)
- but thickness of the tectonic plates varies greatly, from down to 15 km up over the 200 km I mentioned earlier

## Slide 67: 4D alignment – Epochs
One epoch where ITRF2020 coordinates will be equivalent to NATRF2022
at 00:00 on January 01, 2020
ITRF2020 (epoch 2020.0) = NATRF2022 (epoch 2020.0)
Notes: After that, they diverge and continue to do so, we’ll visualize that soon

## Slide 68
Conversion
    change the type of coordinate
    NAD83(2011) latitude & longitude  NAD83(2011) SPCS
  Transformation
    change the datum of coordinate
    NGVD29 height  NAVD88 height
    NAD 27 latitude & longitude  NAD 83(2011) latitude & longitude
Propagation
    change the epoch of coordinate
    NATRF2022 epoch 2020.00 to NATRF2022 epoch 2023.243
Terminology - Changing Coordinates
Notes: Historically NGS has been inconsistent with these top two words.
Going forward, we will use them as:
  Conversion: Meaning to change the type of coordinate without changing the datum or frame
  Transformation: Meaning to change the datum or frame, without changing the type of coordinate

## Slide 69: NCAT
  How will you do that?
Epochs/Time/4D
NGS Coordinate Conversion And Transformation Tool (NCAT)

## Slide 70: NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 71
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 72
NCAT is available via web services

## Slide 73
NCAT is available via web services
Note that each operation is a separate service
Struggling?
Contact us.
We can help!

## Slide 74
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 75
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 76: NCAT source code is on GitHub

## Slide 77: What’s the difference?
NCAT
NSRS Datums
  NAD 27
  NAD 83
  NGVD 29
  NAVD 88
  PRVD 02
  ASVD 02
  NMVD 03
  GUVD 04
  VIVD 09
VDatum
NSRS Datums
Geoid Models
  Add/Subtract from Ellipsoid
Tidal Datums
  MHW, MLLW, MTL
Great Lakes Datum
  IGLD85
ITRF#### ≈ WGS84
Local Tidal (LT)

## Slide 78
Estimated Geometric Change - Horizontal
NAD83 (2011)  NATRF2022
3.6 ft
4.3 ft
3.9 ft
Direction of Shift
4.6 ft
3.0 ft
Notes: What’s the magnitude of the horizontal datum shift across Pennsylvania?
Minimum Shift ~3.75 feet
Maximum Shift ~3.97
Remember this is just an estimation, don’t hold me to the numbers please

## Slide 79: New Lat/Long = New XY
With a new horizontal datum…
There comes a new set of SPCS zones

## Slide 80
State Plane Coordinate System of 1983
SPCS83
North and South Zones as they exist now
Notes: We start with the SPCS83 zones as a frame of reference
NOTE that the color shading of these zones is matched to that of the Preliminary SPCS2022 Zones that follow

## Slide 81
DRAFT

## Slide 82
DRAFT

## Slide 84
State Plane Coordinate System of 2022
SPCS2022
PA stakeholders requested 4-5 zones, which NGS designed, the following are preliminary maps
Notes: The following section illustrates the preliminary SPCS2022 zones
There are 4 zones in the NGS design, per request that we design “4-5 zones required to meet the minimum distortion acceptable” set by our design criteria of 50ppm
NOTE the request also included wording: “It is also requested that PennDOT districts be divded into no more than two zones”

## Slide 85: Stakeholders Involved in PA SPCS2022
PennDOT
PTC
PSLS
PSPE
PA Geospatial Coordinating Board (GeoBoard)
  Geodetic Working Group
County GIS Professionals Association of PA
PA-MAGIC (now Keystone GIS)
PA-MAPPS
Notes: A major component of SPCS2022 are stakeholders
Stakeholders have a role in helping define (and maintain) SPCS2022
Pennsylvania Department of Transportation
Pennsylvania Turnpike Commission
PSLS of course
PSPE – Society of Professional Engineers
The GeoBoard
County GIS Professionals Association of Pennsylkvania
PA Mapping & Geographic Information Consortium
Your State chapter of the Management Association for Private Photogrammetric Surveyors

## Slide 86
Notes: NOTE that the West Zone far surpasses the NGS design criteria of 50ppm

## Slide 87
Notes: This is the first, and likely final, draft of an Oblique Mercator projection for the Preliminary Central Zone
NOTE that even with the

## Slide 88
Notes: This is the second draft of a Preliminary North East Zone

## Slide 89
Notes: This is the second draft of a Preliminary South East Zone

## Slide 94
State Plane Coordinate System of 2022
SPCS2022
NGS will create a Single Statewide Zone for every State, the following is a Preliminary map

## Slide 95
Notes: This Single Statewide Zone designed by NGS is color shaded to match the following section of slides that show UTM Zones linear distortion values
It is known that some user communities with large areas of responsibility choose to maintain geospatial data and work in UTM
This graphic as compared to the UTM serves to highlight in SPCS2022, users will see better performance (lower linear distortion) if they choose to work in the SPCS2022 Single Statewide Zone rather than one of the UTM Zones that fall within Pennsylvania

## Slide 96
UTM (NAD83) Zones as
UTM
The following are maps using existing UTM zones as a Single Statewide Zone
(included to highlight the lower performance as compared to Preliminary NGS Zone)

## Slide 99
Notes: The NGS designed preliminary single statewide zone is included again here at the end for easier visual comparisons.

## Slide 100
Notes: Reminder that you don’t have to cutoff data at any SPCS zone extent
 just need to understand that they’re designed with certain extents in mind

## Slide 101: SPCS2022 Zone Layers in PA
Both Single Statewide and Multi-Zone Layers will coexist
Think about your data, your goals, your customers
  Remember that geographic coordinates are your friend!
Smaller zones not “the best” … it all depends on usage & goals

## Slide 102: Which is best?
Each has strengths and each has weaknesses.
Single Statewide Zone Layer
Multi-Zone Layer

## Slide 103: SPCS2022 Zone Layers and LDPs
Each state may have max of 3 zone “layers”
  One layer must be statewide zone
    Pennsylvania Single Statewide
  Other layers have two or more zones
    Pennsylvania Multi-Zone
  A third layer can exist, but must be discontinuous coverage
    Left open for possibilities in Pennsylvania
      Low Distortion Projections (LDPs) for specific areas?

## Slide 104: Pennsylvania Coordinate System Law
Problems
Designates specific zones
Parameters of projections included
Restricts datum usage to 1983 or 1927
Unit of measure designated as Survey Foot
Anyone familiar with the requirement that SPCS coordinates in recorded land records must be certified by the surveyor?
Act of Dec. 16, 1992, P.L. 1224, No. 161

## Slide 105
State Plane Coordinate System of 2022
SPCS2022
Not just Pennsylvania

## Slide 106: Number of SPCS2022 zones (preliminary)
CONUS, Alaska, and Hawaii
Three island zones not shown:
Puerto Rico and U.S. Virgins Islands
American Samoa
Guam and the Commonwealth of the Northern Mariana Islands

## Slide 107: SPCS2022 linear distortion (prelim)
846 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 108
The Survey Foot is dead!
Long live the Survey Foot!
US Survey Foot was deprecated 31 December 2022… now what?!?

## Slide 109
Deprecated 31 December 2022
Which begs the question
  What should you be doing now?
What happened to the US Survey Foot?

## Slide 110: What should you be doing now?
Ask the right questions
  Does state law specify US Foot for SPCS83?
    40 states do that we know of
  Does it specify US Foot for boundary surveys? (Does that matter?)
    We’re not tracking that, it’s not NSRS-related
Prepare for this along with new datums
  GeoBoard Geodetic Working Group
    Anyone always welcome to any meeting/discussion
    Update Monday evening is that it will likely be un-opposed

## Slide 111: What should you be doing now?
Prepare for this along with new datums
Understand the difference between sft and ift
  2 parts per million
Understand this is not enforced
  Neither NIST or NGS are a regulatory agency
  We support education/outreach of course
  But OPUS, NCAT, etc. will not have US Survey Foot options for output in SPCS2022 zones

## Slide 112
1,000,000.00 sft = 999,998.00 ift
10,000,000.00 sft = 9,999,980.00 ift
1,000.00 sft = 999.998 ift (can you measure that?)
International  1 ft = .3048 m
US  1 ft = .30480061 m (approx.)
2 parts per million (ppm)?

## Slide 114
The Survey Foot is dead!
Long live the Survey Foot!
US Survey Foot was deprecated 31 December 2022…
But it will always be available in NGS tools for NAD83 and NAD27 coordinates

## Slide 115
National Geodetic Vertical Datum
of 1929
NGVD29
was replaced by

## Slide 116
North American Vertical Datum
of 1988
NAVD88
will be replaced by

## Slide 117
North American-Pacific Geopotential Datum of 2022
NAPGD2022
(pronounced: nap-jee-dee)

## Slide 118: NAPGD2022
Geopotential
  gravity based
  no leveling used to define it (none!)
GNSS is your access
  collect data & submit it to OPUS
  no leveling necessary
Global Mean Sea Level (GMSL) based
  geoid change when sea level threshold crossed

## Slide 119
NAVD88 geoids
versus
NAPGD2022 geoids

## Slide 120
  Gravimetric
  Hybrid
Two types of geoid models
Notes: -believe it or not there’s more than 2 types, but the 2 types you’ll see NGS publish are…

## Slide 121
  Gravimetric geoid is created from “scratch” with various types of gravity data
      USGG2003, USGG2009, USGG2012, xGEOID19
  Hybrid geoid is simply a gravimetric geoid then best fit some vertical datum… like NAVD88
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 122
      USGG2003, USGG2009, USGG2012, xGEOID19
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 123: Gravimetric vs. Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid

## Slide 124: NAVD88 uses a Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid

## Slide 125: NAPGD2022 uses a Gravimetric Geoid
  Datum zero surface aligned to Global Mean Sea Level (GMSL)
Concept
topographic surface
datum zero
surface
gravimetric geoid
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 126
equipotential surfaces
(equal gravity)
ground surface
Why leveling is not part of NAPGD2022
…but will still be important for you.
Geoid at Site Scale

## Slide 127
Why leveling is not part of NAPGD2022
…but will still be important for you.
ground surface
equipotential surfaces
(equal gravity)
Geoid at Continental Scale

## Slide 128: Why leveling is not part of NAPGD2022
We are determining height differences across the whole continent
  Large Area
  Gravity varies due to: geology, water, etc.
You are determining height differences across your area/site
  Small Area (as compared to CONUS)
  Gravity does not change that much locally

## Slide 129: Why leveling is not part of NAPGD2022
When you’re working on a site, you need high accuracy relative height differences
  Geoid model is not able to provide that
  So don’t toss out your level come 2025!
What about if submitting data to NGS?
  Yes, we will accept leveling, but…
  GNSS ties will be required
…but will still be important for you.

## Slide 130: Sea Level Change and the Geoid
GMSL
Geoid
Threshold Level
H2020.000
H2085.000
Threshold Level is published as 20 cm
Process is repeated as GMSL changes
Notes: The illustrated strategy will be adopted at NGS. An animated characterization of this approach
What this means is that NGS will decouple the geoid from GMSL, until they have diverged by some threshold amount, currently defined as 20cm.
When that threshold is reached a new geoid will be defined and held fixed until reaching next threshold. In this way, the impact of the change of GMSL is accounted for in the heights of the NSRS, while the appearance of stability is maintained for “decades at a time” (BP2 Section 14).
If we calculate how long that might be based on existing rates of sea level rise of 3ish mm/yr then we’re talking ~60 years

## Slide 131
Estimated change in orthometric heights from NAVD88 to NAPGD2022
(NAPGD2022 approximated using xGEOID16B)
Change in PA:
At least -0.6 feet
At most -2.0 feet
Notes: In Ohio, from just under a foot to almost 2 feet
Quite a bit of variation, but average of 1.5 foot shift down
Change in Pennsylvania:
At least -0.6 feet
At most -2.0 feet

## Slide 132
Estimated change in orthometric heights from NAVD88 to NAPGD2022
OPUS Extended Solution Report

## Slide 133
Estimated change in orthometric heights from NAVD88 to NAPGD2022
OPUS Extended Solution Report
  Scroll all the way to the bottom…

## Slide 134: Preparing for NAPGD2022
Inventory heights in your data/datasets
  Have you mix & matched geoid models?
    Are you tracking levees or other flood control?
    Are you managing subsurface utilities?
      Access covers, junction boxes, cleanouts, etc.
    Maybe geoid differences aren’t even significant?
      VADOT story…
  Know your goals, know your data.

## Slide 135: Preparing for New Datums
Know the epoch of your data/datasets
  consider how you will track this
    full to-the-second timestamp on every feature?
      Modern survey equipment makes this possible
    labeling a year for each dataset?
      Easy to add to workflows, datasets/databases, folders
    something in-between that works for your needs?
2023.1957
2023:27
20230127
Epoch nomenclature is your choice

## Slide 136: Preparing for New Datums
Reprocessing your data
  perfect world = everyone reprocesses everything
    what does this mean?
      consider an ALTA w/topo
        start over with the onsite GNSS-based control
        reorient all your shots/ties (hopefully linked)
        recreate all the drainage features in new datum
    unrealistic! … and unnecessary for majority users
Notes:   Reprocessing your data
    in a perfect world, everyone would reprocess data
        consider a final product like you use everyday - a hydro-enforced DEM
          starting fresh with the raw GNSS/IMU processing
          generate new ellipsoid height point clouds
          recreate all the drainage features in new datum
    this is totally unrealistic  both from a financial and programmatic perspective

## Slide 137: Preparing for New Datums
Transforming your data
  NCAT - NGS Coordinate Conversion and Transformation Tool
    available now: ASCII upload, Web Services, GitHub
    ask your software provider(s) about integration
      we envision this as most popular method of access
      Industry Workshops held in 2021 and 2022
        All the well known commercial names attended
        Plus some open-source advocates
Notes: Transforming your data
NCAT - NGS Coordinate Conversion and Transformation Tool
available now: ASCII upload and Web Services
ask your software providers about integration
we envision this as most popular method of access
Industry Workshop held this year – esri, trimble, bluemarble, all the major well known names were represented
labeling a year for each dataset?
something in-between that works for your needs

## Slide 138: Preparing for New Datums
What can you do to ensure your control will get coordinates in the new datums on rollout?
Re-observe and submit the data to NGS
  must be submitted by 30 September 2023
Options to submit your data:
  OPUS Share  4+ hrs static data; 2 photos; mark ties
    rinse & repeat … as we need redundancy
  OPUS Projects  2+ hrs static GPS data
   5+ minutes RTN-GNSS data, 3x per mark
  Also: photos, field logs, descriptions, survey report
Notes: -OPUS Share requires 4+ hrs static data; 2 photos; and a brief description of reference ties (not a full IDB “from the post office”)
 NOTE THAT OPUS SHARE OPTION REQUIRES 2 OBSERVATIONS
 WHY? WE REQUIRE REDUNDANCY FOR ANY OBS THAT GO INTO OUR DATABASE
-OPUS Projects  2+ hrs data; photos; full IDB style descriptions via WinDesc (*MUST USE WINDESC*)

## Slide 140: Additional Resources

## Slide 141
geodesy.noaa.gov/ADVISORS/
Regional Geodetic Advisor Program
14 RGAs across country
We are here to support:
  You
  Your constituents
  Our Federal Partners
Questions about
NSRS Modernization?
  Reach out now
  Be prepared
Notes: -14 Regional Advisors across the country and Territories
-our advisors homepage up there at the top, also easy to find us by querying any major search engine for “ngs advisors”

## Slide 142
Educational Videos
<5 minutes
Online Lesson
(via MetEd/COMET)
~1 hour
NGS homepage: geodesy.noaa.gov
Notes: Educational videos and online tutorials –
Our library of lessons and videos are great resources, and will reinforce a lot of information we covered today.
The videos are just 3-5 minutes long.
the lesson is a deeper dive but still only takes an hour.

## Slide 143
Click this icon on homepage
Email Subscriptions
*Only 1-2 messages per month*
NGS News
  Includes quarterly NSRS Modernization newsletter
Webinar Series
Training
GPS on Benchmarks

## Slide 144
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486
https://geodesy.noaa.gov/ADVISORS/
-use any major search engine: “NGS advisors”

## Slide 145
Scan to save my contact info on your phone