## Slide 1: Welcome to the Alpha Zone
A Preview of State Plane 2022
Michael Dennis
Krishna Tadepalli
NGS Webinar Series
July 20, 2023
Notes: You are about to enter another dimension, a dimension where the curved surface of the earth is made flat, where coordinates are distorted and distances are not what they seem. Welcome, to the Alpha Zone!

## Slide 2: Poll question
Do you use the State Plane Coordinate System?
795 of 1311 attendees responded

## Slide 3: Poll question
Are you associated with any of the following SPCS2022 stakeholder groups in your state? (select all that apply)
835 of 1311 attendees responded

## Slide 4: Poll question
Do you scale State Plane coordinates to bring them “to ground” (i.e., to reduce linear distortion at the topographic surface)?
855 of 1311 attendees responded

## Slide 5: State Plane Coordinate System of 2022 (SPCS2022)
Part of modernizing the National Spatial Reference System (NSRS)
Third generation of State Plane
  First in 1930s (SPCS 27), second in 1980s (SPCS 83)
  Same 3 map projection types
  Same ellipsoid as SPCS 83 (GRS 80)
Same as existing State Plane, but different…
  Based on new terrestrial reference frames instead of NAD 83
  More zones, most designed by state stakeholders
  Designed to reduce linear distortion at topographic surface (i.e., reduce difference between “grid” and “ground” distances)
Transverse Mercator
Hotine Oblique Mercator
Lambert Conformal Conic

## Slide 6: State Plane Coordinate System of 1983

## Slide 7: State Plane Coordinate System of 2022

## Slide 8: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 9: Number of SPCS2022 zones (preliminary)
Designs by NGS
  165 zones
  Includes 54 statewide zones…
  …and 3 “special use” zones (in more than one state)
Designs by state stakeholders
  802 zones in 28 states
Total = 967 zones for 56 states and territories
Compare to 125 zones in existing State Plane

## Slide 10: SPCS2022 distortion design philosophy
Linear distortion minimized at topographic surface (not ellipsoid surface)
  Purpose: reduce difference between projected “grid” and actual “ground” distances
  Population distribution also taken into account in NGS designs
What is linear distortion?
  Map projection “scale error” at topographic surface
  Unique (i.e., same in every direction) only for conformal projections
  Given here in parts per million (ppm) = mm of distortion per km
Linear distortion | = | Projected minus actual distance | 
 |  | Actual distance | 

## Slide 11: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio | Examples
20 ppm | 2 cm/km | 0.11 ft/mile | 1:50,000 | Typical “low distortion projection” limit
50 ppm | 5 cm/km | 0.26 ft/mile | 1:20,000 | Minimum distortion for designs by NGS
100 ppm | 10 cm/km | 0.53 ft/mile | 1:10,000 | Historic State Plane distortion design limit
400 ppm | 40 cm/km | 2.11 ft/mile | 1:2,500 | UTM distortion design limit

## Slide 12: Poll question
Do you use “low distortion projections” (LDPs)?
850 of 1311 attendees responded

## Slide 13: Distortion design performance
Performance is range of ±distortion for a zone (e.g., ±50 ppm)
Range must include at least all of the following:
  90% of population
  75% of cities and towns (by location only, not by population)
  50% of total zone area
Following ranges used by NGS for distortion design criteria (in ppm):
  ±5, ±10, ±20, ±30, ±40, ±50, ±75, ±100, ±150, ±200, ±300, ±400 ppm, etc.
  Performance is actual value for zone or group of zones
Zones designed by NGS typically limited to ±50 ppm design criterion
  “Low distortion projection” (LDP) zones (e.g., ±20 ppm) designed by stakeholders

## Slide 14
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±370 ppm
Performance percentages:
90% population
91% cities & towns
86% total area
Mean weighted by population: -99 ppm
GREEN: grid = ground (within ±50 ppm or ±0.26 ft/mile)
Grid versus ground distance
BLUE: grid SHORTER than ground
RED: grid LONGER than ground

## Slide 15
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)

## Slide 16
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)

## Slide 17
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)

## Slide 18
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±45 ppm
Performance percentages:
90% population
87% cities & towns
69% total area
Mean weighted by population: -4 ppm

## Slide 19
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±159 ppm
Performance percentages:
90% population
85% cities & towns
59% total area
Mean weighted by population: -75 ppm

## Slide 20
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±45 ppm
Performance percentages:
90% population
87% cities & towns
69% total area
Mean weighted by population: -4 ppm

## Slide 21: When will SPCS2022 be done?

## Slide 22: Alpha preliminary products

## Slide 23: Alpha preliminary release
Public release of preliminary Modernized NSRS products and services
  Preview of Modernized NSRS for NGS partners and customers
  ONLY used for Modernized NSRS
SPCS2022 is first alpha product
  Possible because SPCS2022 design is nearly done
  More coming as modernization products get closer to completion
Web pages
  Alerts on various production NGS pages (New Datums page, SPCS pages)
  Overall alpha Modernized NSRS page
  SPCS2022 alpha web pages

## Slide 24: Alpha products are NOT final products!
Preliminary
For illustrative purposes only
Not authoritative
Under active development
Subject to change without notice
Feedback to: ngs.feedback@noaa.gov
https://alpha.ngs.noaa.gov/index.shtml

## Slide 25: Alpha SPCS2022 Home
https://alpha.ngs.noaa.gov /SPCS/index.shtml
Gives date last updated (on all SPCS2022 pages)
Links to other SPCS2022 pages
Link to online interactive maps (SPCS2022 Experience)
Link to alpha NCAT
Link for providing feedback

## Slide 26: Zone Information
Interactive tables
  Zone definitions
  Example coordinates
Downloadable data and other tables will be added later
Note new protocol for grid origins
  Metric with exact whole number inter-national foot value
  Specified in SPCS2022 Procedures
  Stakeholder can adopt values they prefer

## Slide 27: Zone definitions and design status

## Slide 28: Zone definitions and design status

## Slide 31: Example coordinates and distortion values

## Slide 35: Linear Distortion Maps
Static map images
  Include performance statistics
  Includes SPCS 83 for comparison
Only CONUS and Alaska
  These and other areas will be on future “Download Maps & Data” page
  Will include data used to create maps
Links to online interactive maps and alpha NCAT
High resolution images when click on thumbnail

## Slide 38: ArcGIS Online SPCS2022 Experience
Online interactive maps
Shows distortion and gives projection definitions
  Zone parameters not all given to full precision
  Cannot get distortion values from maps
Plan to create SPCS 83 version for comparison (maybe UTM, too)

## Slide 45: Poll question
Do you use the NGS Coordinate Conversion and Transformation Tool (NCAT)?
816 of 1311 attendees responded

## Slide 47
NGS Coordinate Conversion and Transformation Tool
(NCAT)
Alpha

## Slide 48
NCAT
A one-stop solution for coordinate conversion and transformation
Revamps and modernizes Geodetic Toolkit
Toolkit modernization is an integral part of NSRS modernization

## Slide 49
NCAT
Multiple ways of access:
Single point conversion/transformation
Multi-point conversion/transformation
NCAT download (for conversions only)
NCAT + grids download (for conversions and transformations)
NCAT API
Grids download ( for custom software)

## Slide 50
NCAT
API vs Download
API | Download
Platform independent | Platform independent
Internet access required | No internet access required
Updates are automatic | Updates are manual
Command line access | Command line access
Access is through API calls | Access is through library calls
Backward compatibility | Backward compatibility may not be guaranteed

## Slide 51
NCAT Conversion
Supports geodetic to projected coordinate (SPC,UTM,USNG,XYZ) conversion and vice versa
Supports conversion between two SPC zones or two UTM zones for all access modes
Allows override to auto picked zones
Auto pick of SPC zone option is not available from the download package

## Slide 52
NCAT Transformation
Uses Nadcon 5.0 for horizontal and Vertcon 3.0 for vertical transformation
Transformation only available for supported regions
Visit Nadcon 5.0, Vertcon 3.0, or NCAT API pages to learn more

## Slide 53
NCAT API
Delivered in JSON format
Easy to consume and parse
An API link for metadata available for keys used in JSON
Rate limits apply

## Slide 54
NCAT Web Interface
Dynamic user interface, responsive design
Supports multiple export formats
Simple format for upload
Custom format for export

## Slide 55
NCAT Tutorial
Available under the “About..” tab
Part 1- NCAT Conversions
Part 2- NCAT Transformations

## Slide 56
NCAT Live Demo

## Slide 57: Learn More
NOAA Special Pub NOS NGS 13
Paper on SPCS2022
Updated SPCS2022 Policy and Procedures
Other information and resources
  Legislation
  SPCS2022 definitions in registries
  UTM and USNG
Webinars

## Slide 58: NSRS Modernization
Alpha site is ONLY for NSRS Modernization
Rollout 2025
More to it than just SPCS2022…
  Deprecation of U.S. survey foot
  Terrestrial reference frames
  Geopotential datum
  Time-dependence
  Reference and survey epoch coordinates
  And more…
PRELIMINARY

## Slide 59: That’s great, but when will SPCS2022 be done?
SPCS2022 Rollout of Modernized NSRS in 2025
But SPCS2022 design will be done sooner
  Getting feedback now from stakeholders and others now
  In process of updating projection algorithms
  Finalize designs by end of 2023 or shortly after
  Get Federal Geodetic Control Subcommittee approval in early 2024
Provide final completed designs to the world in 2024!

## Slide 60: Where to learn more…
geodesy.noaa.gov
Thank you!

## Slide 61: Poll question
What is your profession?
756 registrants responded