## Slide 1: GeMS
Geoid Monitoring Service
NGS Project to estimate time-dependent quantities and incorporate into vertical reference system (NAPGD 2022)
Quantities:
Geoid Time Rate of Change – secular trend from GRACE (NASA GSFC mascon v02.4, Luthcke, et al. 2013))
Notes: Stress: need to validate how well this changes reflect what is happening on the ground.

## Slide 2: Causes of Geoid Change
Any mass change or redistribution
Glacial isostatic adjustment (GIA)
present day ice-mass changes
changes in hydrology (including ground water storage, snow, etc.)
large earthquakes
volcanic eruptions
Mass Change in cm water equivalent (cm w.e.) – secular trend from GRACE (NASA GSFC mascon v02.4, Luthcke, et al. 2013))
Notes: Stress: Need a lot of mass change over large areas to get ‘significant’ geoid change

## Slide 3
NASA/GFZ missions to monitor temporal gravity field at 200 km wavelengths
GRACE: 2002 – 2017
GRACE-FO: 2018 –
Foundation for GeMS models. Use monthly gravity fields to estimate a trend and produce
GRACE/GRACE-Follow-on
GRACE/GRACE-FO – Twin satellites that measure distance between one another at few mm (a tenth of the thickness of a human hair)
Relationship between gravity change, geographic size of change, and geoid change. Combinations to the right of the blue line will cause a 1 cm geoid change.

## Slide 4
Monthly time series from GRACE/GRACE-FO
Temporal signatures: trend, sinusoids, instantaneous jump, (& residual)
Looking at one of the mascons….

## Slide 5: Annual Amplitude
Seasonal geoid model…
Amplitudes are only 4-5 mm in North America
Amazon River basin in South America has 10+ mm
Geoid change annual amplitude (mm) from GRACE
Notes: Stress: Need a lot of mass change over large areas to get ‘significant’ geoid change

## Slide 6: Episodic Events
Earthquakes, Volcanoes, Landslides…
Case by case
Possibly warrant a geodetic response
Very rarely occur at levels of significance
  1992 Landers M7.3 Earthquake produced ~0.1 mm
  1964 Alaska M9.2 had ~10 mm
Modeled geoid change in mm for (a) the 1964 Alaska earthquake and (b) the 1992 Landers earthquake. (from Jacob, et al., 2012)
Notes: Stress: Need a lot of mass change over large areas to get ‘significant’ geoid change

## Slide 7
GeMS Products:
Relationship to NSRS Modernization
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
  DEFLEC2022
  GRAV2022
  DEM2022
  IGLD 2020
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical
Static Geoid Model (SGEOID2022)
Dynamic Geoid Model (DGEOID2022)
SDEFLEC2022
DDEFLEC2022
SGRAV022
DGRAV2022
SDEM2022
DDEM2022
Notes: Bold elements are provided by GeMS…

## Slide 8
Final Takeaway:
xGEOID19 will likely contain DGEOID component from GeMS
kevin.ahlgren@noaa.gov